Bunch-to-Bucket (B2B)
Transfer System for FAIR
Jiaoni Bai
Thibault Ferrand
23.05.2016
May 23, 2016 | GSI | CSCO & PBRF | Jiaoni Bai & Thibault Ferrand |

---
Outlines
- Introduction (Bai)
- Kicker and bucket pattern (Bai)
- B2B transfer procedure (Bai)
- Synchronization methods (Bai)
- Example: U28+ B2B transfer from SIS18 to SIS100 (Bai)
- Functional implementation (Thibault)
- Task sharing (Thibault)
- Functional specification and requirements (Thibault)

---
Introduction
Bucket : a bucket defines the potential
well in (Ekin,t) - phase space, where
the particles can be trapped.
Bunch : a bunch defines the packet of
particles gathered within a bucket.
Focus mainly on the B2B transfer from SIS18 to SIS100
Firstly tested in B2B transfer from ESR to CRYRING

---
Kicker & Bucket pattern
Assumption:
Virtual cavity is located at the extraction/injection kicker position.
There is no distance between two virtual cavities.
Bucket #1 and #2
U28+
#2
SIS18
~1
# 1
SIS18 revolution
frequency marker @SIS18
time
SIS100 revolution frequency marker @SIS18
Extraction Kick
time
SIS100 revolution frequency marker @SIS100
time
Injection Kick
SIS100
#1

---
Kicker & Bucket pattern
#3
#4
#2
Consideration:
1. Bucket pattern (#3 and #4)
#1
# 1
SIS18 revolution
frequency marker @SIS18
time
1
SIS100 revolution frequency marker @SIS18
size 12{ ital "delay" rSub { size 8{ ital "bucket"} } } {}
Extraction Kick
time
1
SIS100 revolution frequency marker @SIS100
size 12{ ital "delay" rSub { size 8{ ital "bucket"} } } {}
Injection Kick
time

---
Kicker & Bucket pattern
Consideration:
1. Bucket pattern (#3 and #4)
2. Time Of Flight (TOF)
TOF
# 1
SIS18 revolution
frequency marker @SIS18
TOF
time
1
2
SIS100 revolution frequency marker @SIS18
TOF
time
1
Extraction Kick
2
SIS100 revolution frequency marker @SIS100
Injection Kick
time

---
Kicker & Bucket pattern
Consideration:
1. Bucket pattern (#3 and #4)
2. Time Of Flight (TOF)
3. Distance between virtual cavity and extraction/injection kicker position (tsrc and ttrg )
tsrc
TOF
ttrg
# 1
tsrc+TOF+ttrg
SIS18 revolution
frequency marker @SIS18
time
1
2
3
SIS100 revolution frequency marker @SIS18
ttrg
TOF
time
1
Extraction Kick
2
3
ttrg
SIS100 revolution frequency marker @SIS100
time
Injection Kick

---
Kicker & Bucket pattern
Consideration:
1. Bucket pattern (#3 and #4)
2. Time Of Flight (TOF)
3. Distance between virtual cavity and transport line (tsrc and ttrg )
4. Extraction and injection kicker delay (Dext and Dinj)
tsrc
TOF
ttrg
# 1
tsrc+TOF+ttrg
SIS18 revolution
frequency marker @SIS18
time
4
1
2
3
SIS100 revolution frequency marker @SIS18
ttrg
TOF
size 12{D rSub { size 8{ ital "ext"} } } {}
time
1
Extraction Kick
2
3
4
ttrg
SIS100 revolution frequency marker @SIS100
size 12{D rSub { size 8{ ital "inj"} } } {}
time
Injection Kick

---
Procedure for the B2B transfer system
SIS100
Supply
room
Cavity input signal
Virtual
cavity
Virtual
cavity
Location at the ring corresponding to Group DDS reference rf signals
1. Synchronization window calculation
EVT_START_B2B
Synchronization window
Phase
prediction
1
B2B Status
check
time
Ext kick
Extract kick info
Phase info from
SIS100 to SIS18
Synch window from
SIS18 to WR network
B2B status
Beam injection ts
WR network
Inject kick info
Synchronization window
Phase
prediction
Inj kick
SIS100

---
Synchronization methods
Phase shift method
Synchronization window
Features
Adiabaticity
Infinite synchronization window
B2B transfer time is predictable
Phase jump
Frequency beating method
Features
Bunch and bucket center Mismatch
Mismatch within the synchronization window is better than 1°
Only choice for some pair of machines
Automatically beating
Bunch
Bucket

---
Example: U28+ B2B from SIS18 to SIS100 with the phase shift method
From SIS18, four batches of the U28+ at 200 MeV/u, each of two bunches,
are injected into eight out of ten buckets of SIS100.
U28+	SIS18	SIS100
Energy	200Mev/u	200Mev/u
Circumference	216.72 m	1083.6m
Ratio	5
Cavity frequency	1.572MHz	1.572MHz
h	2	10
Phase shift	Parabola modulation for SIS18 / Max 64Hz/ms / Offset 150Hz / 7ms for phase shift 180°
Synchronization window
Phase
prediction
1
B2B Status
check
time
Ext kick
WR network
Extract kick info
Phase info from
SIS100 to SIS18
Synch window from
SIS18 to WR network
B2B status
Beam injection ts
Inject kick info
SIS100
Synchronization window
Phase
prediction
Inj kick

---
Example: U28+B2B from SIS18 to SIS100 with the frequency beating method
U28+	SIS18	SIS100
Energy	200Mev/u	200Mev/u
Circumference	216.72 m	1083.6m
Ratio	5
Cavity frequency	1.572MHz	1.572MHz
h	2	10
Frequency beating	Detune 200Hz for SIS18 / Beating period 5 ms / Bunch and bucket center mismatch ± 0.46°
Synchronization window
Phase
prediction
1
B2B Status
check
time
Ext kick
WR network
Extract kick info
Phase info from
SIS100 to SIS18
Synch window from
SIS18 to WR network
B2B status
Beam injection ts
Inject kick info
SIS100
Synchronization window
Phase
prediction
Inj kick

---
Functional specification and implementation

---
Kicker electronics
EVT_B2B_STATUS
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
1. Phase measurement & Prediction
WR network
Kicker electronics
SIS100
1. Phase measurement & Prediction
Time
Ref SCU
Group DDS
400us ~ 1ms
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction

---
B2B
SCU
PAP
PSM
PCM
SR
Switch
Matrix
OSA
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC
DSP
RF Supply Room

---
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
EVT_START_B2B
1. Phase measurement & Prediction
Trigger decision
Phase correction
Signal reproduction
EVT_B2B_STATUS
2.Phase info from SIS100 to SIS18
WR network
Kicker electronics
SIS100
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
500us

---
WR Switch
DM
Copy
SCU
REF
SCU
B2B
SCU
Trigger
SCU

---
Kicker electronics
EVT_START_B2B
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase info from SIS100 to SIS18
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
Phase shift method
3.Calculation synch window and phase correction (phase shift)
EVT_B2B_STATUS
WR network
Kicker electronics
SIS100
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
5us

---
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
4.Transfer phase correction value to signal reproduction module
4. Produce phase shift profile
4. Beginning of the synchronization window
Phase correction
WR network
Kicker electronics
SIS100
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase info from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
2ms
Phase shift method

---
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
5.Reproduction of the revolution signal of SIS100 at SIS18
Signal reproduction
5. Phase shift for group DDS
5.Reproduction of the revolution signal of SIS100 at SIS18
EVT_B2B_STATUS
WR network
Kicker electronics
SIS100
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
<7ms
Phase shift method

---
B2B
SCU
PAP
PSM
PCM
SR
Switch
Matrix
OSA
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC
DSP
RF Supply Room

---
Trigger
SCU
PCM
SR
TD
Kicker
SCU
KE
Kicker Supply Room

---
EVT_START_B2B
Kicker electronics
SIS18 Trigger SCU
6.Produce trigger signal
Trigger decision
Phase correction
Signal reproduction
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
5. Reproduction of the revolution signal of SIS100
    Phase shift for group DDS (phase shift)
EVT_B2B_STATUS
WR network
Kicker electronics
SIS100
6.Produce trigger signal
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction

---
Trigger
SCU
PCM
SR
TD
Kicker
SCU
KE
Kicker Supply Room

---
Trigger
SCU
PCM
SR
TD
Kicker
SCU
KE
Kicker Supply Room

---
Kicker electronics
EVT_START_B2B
7.Trigger timestamp & Kicker timestamp
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
5. Reproduction of the revolution signal of SIS100 at SIS18
    Phase shift for group DDS (phase shift)
6. Produce extraction and injection trigger signals
EVT_B2B_STATUS
WR network
Kicker electronics
SIS100
7.Trigger timestamp & Kicker timestamp
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction

---
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
5. Reproduction of the revolution signal of SIS100 at SIS18
    Phase shift for group DDS (phase shift)
6. Produce extraction and injection trigger signals
7. Collection of trigger timestamp and Kicker timestamp
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
EVT_B2B_STATUS
8.SIS18 trigger ts & kicker ts to SIS18 B2B SCU
WR network
8.SIS100 trigger ts & kicker ts to SIS18 B2B SCU
Kicker electronics
SIS100
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
11ms

---
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
9.B2B transfer status check
EVT_B2B_STATUS
WR network
Kicker electronics
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
5. Reproduction of the revolution signal of SIS100 at SIS18
    Phase shift for group DDS (phase shift)
6. Produce extraction and injection trigger signals
7. Collection of trigger timestamp and Kicker timestamp
8. Transfer SIS18 trigger timestamp and kicker timestamp to
    SIS18 B2B SCU
SIS100
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
5us

---
Kicker electronics
EVT_START_B2B
SIS18 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
EVT_B2B_STATUS
10.B2B transfer status and beam injection timestamp
WR network
Kicker electronics
EVT_START_B2B
1. Phase measurement & Prediction
2. Phase information from SIS100 to SIS18
3. Calculation synchronization window and phase correction
    (phase shift)
4. Transfer phase correction value to signal reproduction module
    Produce phase shift profile (phase shift)
    Send beginning of the synchronization window to WR network
5. Reproduction of the revolution signal of SIS100 at SIS18
    Phase shift for group DDS (phase shift)
6. Produce extraction and injection trigger signals
7. Collection of trigger timestamp and Kicker timestamp
8. Transfer SIS18 trigger timestamp and kicker timestamp to
    SIS18 B2B SCU
9. B2B transfer status check
SIS100
Time
Ref SCU
Group DDS
SIS18 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction
SIS100
Ref SCU
Group DDS
SIS100 Trigger SCU
Trigger decision
Phase correction
Signal reproduction
SIS100 B2B SCU
Phase correction
Phase shift
Phase advance prediction
Signal reproduction

---
Block diagram
Extraction Kicker Supply Room
RF Supply Room
WR Switch
OSA
Switch
Matrix
WR Switch
DSP
SIS100
Injection Kicker Supply Room
BI
SCU
WR Switch
WR Switch
DM
WR Switch
SIS100
RF Supply Room 3
Switch
Matrix
OSA
OSA
OSA
Switch
Matrix
Switch
Matrix
SIS100
RF Supply Room 2
DSP
SIS100
RF Supply Room 1
B2B
SCU
PAP
PSM
PCM
SR
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC
Kicker
SCU
KE
Trigger
SCU
PCM
SR
TD
Kicker
SCU
KE
Trigger
SCU
PCM
SR
TD
B2B
SCU
PAP
PSM
PCM
SR
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC
B2B
SCU
PAP
PSM
PCM
SR
B2B
SCU
PAP
PSM
PCM
SR
REF
SCU
Gp DDS
rf1
Gp DDS
rf2
Gp DDS
rf3
Gp DDS
rf4
Copy
SCU
SYNC

---
Task sharing
Hardware VIEW
SCU
MHU
WR network
DM
Infrastructure (LM32, VHDL code)
DDS
PBRF
PBRF
Software VIEW
Synchronization window calculation (B)
Phase shift and correction calculation (B)
B2B status check (B)
Send/receive to/from WR network (B)
B2B FESA configuration (B)
Phase shift profile and phase shift (T)
Signal reproduction (T)
Phase advance measurement and prediction (T)
CSCO (Hardware)
CSCO (Timing group)
CSCO (Timing group)
CSCO (Timing group)

---
Functional Requirements
Modular all in rack topology
All B2B transfers for FAIR
Transfer to a fixed target
Phase shift and frequency beating method
Maximum synchronization time. E.g. 10 ms for U28+ from SIS18 to SIS100
Bunch to bucket center mismatch less than 1°.
Timing messages for beam instrumentation (BI)
Inhibit and emergency extraction signals from the Machine Protection System (MPS)
B2B transfer status back to the DM
Flexible bucket filling pattern

---
Thank you for your attention !